## Slide 1: HDR in Cinema: Achievable Contrast
Jean-Philippe Jacquemin
Goran Stojmenovik
HPA
February 2017

## Slide 2: What we will talk about
Introductory definitions
What’s the actual screen contrast given the projector, auditorium and image content?
What level of black detail we can discern at a certain image brightness?
What does this mean in the ‘bigger picture’ – with realistic content?
Wrapping up

## Slide 3: Our previous research
Modelling of achievable contrast and its impact on HDR projection in commercial cinema environments
  Tydtgat et al; SMPTE ATC 2015 (talk and paper)
The perceived intra-frame dynamic range in a cinema environment
  Maes et al; SMPTE ATC 2016 (talk and paper)

## Slide 4: What is projector contrast?
Projector native contrast:
=
Lw
Lb
CRnat=Lw/Lb (:1)
*Need to measure directly in the projector with a directional lux meter
**Very difficult to measure low black levels accurately: need specific equipment
illumination of white field
illumination of black field
(with the same lamp power setting and same lens zoom!)

## Slide 5: What about if there is some content in the image?
“Figure of merit” is ANSI contrast = “checkerboard contrast” *
“White” - <Lw>: Average brightness** of white squares
“Black” - <Lb> : Average brightness of black squares
Contrast = “White”/”Black”
*As a rule, due to lens and other scattering, ANSI contrast is much lower than native projector contrast
** Measured looking directly in the projector, not off the screen
CR ANSI=<Lw>/<Lb> (:1)

## Slide 6: What we will talk about
Introductory definitions
What’s the actual screen contrast given the projector, auditorium and image content?
What level of black detail we can discern at a certain image brightness?
What does this mean in the ‘bigger picture’ – with realistic content?
Wrapping up

## Slide 7: What’s the screen contrast given a projector, auditorium and certain image content?
b. Add scattering (dust, porthole, lens) and diffraction (optics): s%
To calculate CRproj
c. Reflectivity of the auditorium: r% to calculate CRtheatre
a. Native, ‘ideal’ projector sequential contrast:
CRnat
EXIT
Auditorium Contrast Model, aka “THE MODEL”
(SMPTE ATC 2015, Tydtgat et al)

## Slide 8: “ANSI-ish” test patterns
Examples of used test patterns with varying white content a, representing an Average Picture Level (APL)
a= 1% 10% 25% 50%
Projector ANSI contrast is determined by optics scatter;
On-screen contrast in addition takes reflections into account.

## Slide 9: Mathematical model and approximation
(1-s+sa)CRseq+s(1-a)
saCRseq+ (1-sa)
CRproj=
(1+ar)CRproj+(1-a) r
arCRproj+ (1+r-ar)
CRtheatre=
(eq.2)
(eq.1)
CRtheatre= f(CRseq,s,r,a)
For (s+r)<<1 we obtain:
CRtheatre
=
1
CRseq
1
+ a(s+r)
Or,
Screen black
Projector white
=
Projector black
+ a(s+r) x
(+ Ambient light)

## Slide 10: Results: model fit and real-life parameters
s range: 0.5% - 1.8%
r range: 1.1% - 2.5%
s+r range: 1.6% - 4.0%
Theatre | s |  | s+
1 | 0.015 | 0.019 | 0.034
3 | 0.010 | 0.025 | 0.035
4 | 0.005 | 0.011 | 0.016
5 | 0.018 | 0.022 | 0.040
6 | 0.009 | 0.018 | 0.027
7 | 0.008 | 0.021 | 0.029
8 | 0.010 | 0.013 | 0.023
Green circles are actual measurements
The model rocks!
Significant spread in real life parameters.

## Slide 11: Results: Impact on real-life screen contrast
2000:1 projector, screen contrast drops to 200-400:1 @ 10% APL @ avg auditorium

## Slide 12: How does the screen impact on-screen contrast?
Screen type (silver or white) impacts the screen contrast greatly
Typical Silver screens have an TIS (total integrated scatter) of around 50%.
SILVER SCREENS ARE GREY – they absorb 50% of the non-directional illumination.
So the r – coefficient implicitly contains the screen ‘reflectivity’ (TIS) as well, next to the room reflection.
WITH THE SAME ROOM REFLECTION, A SILVER SCREEN WILL REDUCE THE r BY 50% IN COMPARISON WITH WHITE SCREENS:
  SCREEN CONTRAST WILL BE BETTER WITH A SILVER SCREEN!
Screen black
Projector white
=
Projector black
+ a(s+r) x

## Slide 13: What we will talk about
Introductory definitions
What’s the actual screen contrast given the projector, auditorium and image content?
What level of black detail we can discern at a certain image brightness?
What does this mean in the ‘bigger picture’ – with realistic content?
Wrapping up

## Slide 14: Perception experiment setup
Background grey level projection
  0%, 0.5% & 5% (@ 48 cd/m2)
Black plate on the left
  ambient + straylight suppression
4000 cd/m2 LED wall to the right
  0%, 50% & 100%
  Left, Right & Full
  4000 cd/m2 @ full white
36 persons between 18 and 34 years
Black Plate
20x attenuation
1.4m
1.4m
12.6m
LED wall

## Slide 15: Perception experiment
Question to test subjects: “How many squares you see”
Attaining the perceptual black threshold, depending on environment and nearby highlights
Influencing parameters on visibility:
  Background APL–> black, 0,5% and 5% @ 48 cd/m2
  Eye adaptation -> couple of seconds
  LED Peak white level -> range 50 Cd/m2 - 4000 Cd/m2
  Proximity of peak white level -> test in different positions
9x9 pixels,
Randomly spread

## Slide 16: Findings
The HVS can perceive very low levels of black (in ideal environments)
Background adaptation brightness lifts the lowest perceivable level
However:
  Auditorium reflectivity and scatter will produce a black level HIGHER than the visible threshold in most cases, even with an infinite projector contrast
  Increasing APL levels will also increase reflectivity, further increasing the black level
Background (cd/m2) | Detection threshold (cd/m2)
0,0008 | 0,005
0,25 | 0,009
2,5 | 0,015

## Slide 17: What we will talk about
Introductory definitions
What’s the actual screen contrast given the projector, auditorium and image content?
What level of black detail we can discern at a certain image brightness?
What does this mean in the ‘bigger picture’ – with realistic content?
Wrapping up

## Slide 18: What does this mean for a real movie? -Relevant statistics*
*Source: M. Schuck, P Lude RealD paper on SMPTE ATC 2015
Title | Average luminance | Avg lum. cd/m2 (max=48cd/m2)
TinTin | 8.2% | 3.9
Hobbit 1 | 3.7% | 1.8
Shrek 2 | 5.6% | 2.7
Thor | 6.3% | 3.0
Life of Pi | 13.8% | 6.6
KungFu Panda | 5.9% | 2.8
Gulliver's Travels | 11.3% | 5.4
Alice in Wonderland | 6.0% | 2.9
Aggregate Average | 7.6% | 3.6
Standard Deviation | 0.034 | /

## Slide 19: Relevant statistics
In an ‘average’ movie (@ 14fL white)
<0.7 cd/m2
(<1.5% APL)
>1.4 cd/m2
(>10% APL)
Darkest 1/10th of the movie
Brightest 1/10th of the movie

## Slide 20: Different projector performance: It’s all in the ANSI!
Contrast reduces significantly from native to ANSI, depending on optics scatter and auditorium reflections (1% reflectance taken here)
1% APL
10% APL
25% APL
50% APL

## Slide 21: Zoom in on the darker frames
Case with 1% auditorium reflectance – best we measured – and without any audiences!

## Slide 22: What we will talk about
Introductory definitions
What’s the actual screen contrast given the projector, auditorium and image content?
What level of black detail we can discern at a certain image brightness?
What does this mean in the ‘bigger picture’ – with realistic content?
Wrapping up

## Slide 23: Summary
Real-life scattering and reflectivity can seriously impact screen contrast and black level
HVS black detection threshold is very low, but impacted by image APL
… How does this all add together?

## Slide 24: Gluing the pieces together: Screen black level – different projectors and varying image APL

## Slide 25: Future work
What is the impact of actual image brightness distribution on perception?
Eye adaptation?
New technologies?